## Slide 1: Phy 103: Fundamentals of Physics
Chapter 23: Electric Current
Lecture Notes
Notes: Electricity:
Electrostatic: electricity at rest.
Electrical force: Like charges repel. Unlike charges attract.
Electric charge: fundamental electrical property to which the mutual attractions or repulsions between electrons or protons is attributed.
Conservation of charge: electric charge is neither created nor destroyed. The total charge before an interaction equals the total charge after.
Coulomb’s law:
F = k q1q2/d2
If the charge are alike in sign, the force is repulsive; If the charge are unlike, the force is attractive.
Conductors:
Conductors
Insulators
Semiconductors
Superconductors
Charging:
Charging by friction and contact: Electrons can be transferred from one material to another by simply touching.
Charging by induction: Redistribution of electric charges in and on objects caused by the electrical influence of a charged object close by but not in contact.
Charge polarization:
Electrically polarized: the charges are aligned so that one side is slightly more positive or negative than the opposite side in a molecule or an atom.
Electric field: force field that fills the space around every electric charge or group of charge.
E = F/ q
Electric potential:
Voltage = electrical potential energy/charge
Electric potential energy : the energy a charged object possesses by virtue of its location in an electric field
Capacitor: an electrical device, in its simplest form a pair of parallel conducting plates separated by a small distance, that stores electric charge and energy.

## Slide 2: Electric Current
An electric potential difference causes electric charges to move
The flow of electric charge is called electric current
  Positive charge accelerates toward lower electric potential
  Negative charge accelerates toward higher electric potential
The rate of flow of electric charge (I) through a conducting material is the amount of charge (Q) that flows divided by the time (t) it takes to flow, or
I = Q/t
  SI units are coulombs per second (C/s), called amperes (A), where 1 coulomb/sec = 1 Ampere
By convention, electric current is defined as the flow of positive charge flowing from high potential (+) to low potential (-)

## Slide 3: Resistance
The physical property of a material to “impede” the flow of electric charge is called electrical resistance
An object’s resistance (R) depends on:
  Its inherent ability to conduct electricity, its resistivity ()
  The surface area (A): the wider the area the more room for current to flow
  The length (L) of the object: the longer the object the more material the current must be pushed through
R ~ L/A
Conductors (like metals) have low resistance
Insulators (plastics & non-metals) have high resistance

## Slide 4: Ohm’s Law
For a given potential difference (V), the magnitude of electric current (I) depends on the physical properties of the conductor (dimensions and material)
The electric current that will flow through a circuit is
  proportional to the potential difference (V)
  Inversely proportional to the resistance of the circuit
I = V/R {this is Ohm’s Law}
For many substances, R is constant:
R = V/I = a constant value

## Slide 5: Georg Simon Ohm (1789-1854)
German physicist
Originally a secondary school (gymnasium) teacher
  Pursued research to obtain a university post
Studied electricity and the physics of hearing
Most famous work (on “Ohm’s Law”) was published in a book in 1827
Electrical studies were strongly influenced by Fourier’s work on heat conduction

## Slide 6: Electric Power
It takes effort and energy (work) to drive electric charge through a circuit (against its resistance)
The rate of energy (power or P) required to drive electric current through a circuit (or part of a circuit) is proportional
  To the potential difference (V) across
  To the electric current (I) that flows through a circuit
P=VI
The SI units of power are _____
  Volts (V) times amperes (A)
  Joules per second (J/s)
  Watts (W)

## Slide 7: Direct Current (DC) & Alternating Current (AC)
When the power source running an electric circuit moves charge only one direction it is a direct current (DC) circuit
  Current flows from the high potential terminal (+) to the low potential terminal (-)
  In DC circuits, the power source supplies the electrons
  Batteries and photoelectric cells produce DC current
When the power source driving an electric circuit moves charge back-and-forth it is a an alternating current (AC) circuit
  In AC circuits, you supply the electrons
  Our wall sockets typically fluctuate between +170 V and –170 V at a rate of 60 Hz
  The fluctuating voltage has a sinusoidal waveform:

## Slide 8: Alessandro Volta (1745-1827)
Italian physicist & inventor
First person to isolate methane
Fascinated with electricity at an early age
Pioneered the field of electrochemistry
Constructed the first battery to produce electricity (called a voltaic pile)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Nikola Tesla (1856-1943)
Serbian-American inventor & engineer
A major rival of Thomas Edison
Pioneered the use of AC current for commercial power
Sold many of his patents to Westinghouse Corporation
Notable inventions:
  Radio
  Fluorescent lights
  Wireless communication
  Alternating current transmission
  Tesla coil transformer
  An electric automobile (the Pierce Arrow)
  Over 700 patents
“Science is but a perversion of itself unless it has as its ultimate goal the betterment of humanity”

## Slide 10: Electric Circuits
Power supply: provides the electric potential difference between its terminals
  A device that transforms energy from one form of energy (such as chemical) into electrical energy
  Characterized by its electromotive force (V)
    The potential difference or voltage between the terminals
Connecting wires: provide a path for electric current to flow (their resistance is usually very small ~ 0 )
Consumer (or load): any electrical device connected to the circuit (characterized by its resistance, R)
Notes: <number>
<footer>
<header>
<date/time>
As a battery gets old, its internal resistance(r) increases
It dies when its internal potential difference equals its electromotive force

## Slide 11: Electric Circuits
Types of electrical connections:
Series:
  components are connected head-to-tail
Parallel:
  Components are connected head-to-head & tail-to-tail
+
-
+
-