## Slide 1: Phy 103: Fundamentals of Physics
Chapter 25: Electromagnetic Induction
Lecture Notes
Notes: Electricity:
Electrostatic: electricity at rest.
Electrical force: Like charges repel. Unlike charges attract.
Electric charge: fundamental electrical property to which the mutual attractions or repulsions between electrons or protons is attributed.
Conservation of charge: electric charge is neither created nor destroyed. The total charge before an interaction equals the total charge after.
Coulomb’s law:
F = k q1q2/d2
If the charge are alike in sign, the force is repulsive; If the charge are unlike, the force is attractive.
Conductors:
Conductors
Insulators
Semiconductors
Superconductors
Charging:
Charging by friction and contact: Electrons can be transferred from one material to another by simply touching.
Charging by induction: Redistribution of electric charges in and on objects caused by the electrical influence of a charged object close by but not in contact.
Charge polarization:
Electrically polarized: the charges are aligned so that one side is slightly more positive or negative than the opposite side in a molecule or an atom.
Electric field: force field that fills the space around every electric charge or group of charge.
E = F/ q
Electric potential:
Voltage = electrical potential energy/charge
Electric potential energy : the energy a charged object possesses by virtue of its location in an electric field
Capacitor: an electrical device, in its simplest form a pair of parallel conducting plates separated by a small distance, that stores electric charge and energy.

## Slide 2: Electromagnetic Induction
So far we have observed that an electric current produces a magnetic field
Question: Can a magnetic field produce an electric current?
Answer: Yes!
It’s called electromagnetic induction!!
When a magnetic field is changed near a wire loop, a voltage (called electromotive force) is induced in the wire
The resulting voltage generates an electric current
  The size of the voltage depends on how fast you change the magnetic field
  The size of the current depends on the resistance in the wire as well as the induced voltage (remember Ohm’s Law?)

## Slide 3: Faraday’s Law
The product of the area of a loop of wire (coil) times the magnetic field inside the wire is called the magnetic flux (
 = B.A
When the magnetic flux changes, a voltage is induced in the coil. The induced voltage (V) is related to:
  The number of loops (N) in the coil
  The rate at which the magnetic flux is changing (/t) inside the loop(s), or
  Note: the magnetic flux changes when either the magnetic field (B) or the area (A) of the loop changes:
   = A.B or  = B.A
{Faraday’s Law}
Notes:   When either B or A changes:
    B is the change in magnetic field (B) or
    B= Bfinal-Binitial
    A is the change in area of the loop (A) or
    A= Afinal-Ainitial

## Slide 4: Generators & Alternating Current
Electromagnetic induction can be used to produced electricity
  A device that does this is called an electrical generator
  Generators convert mechanical energy into electrical energy
  Mechanical energy is utilized to either:
    rotate a magnet inside a wire coil
    Rotate a wire coil inside a magnetic field
  In both cases, the magnetic flux inside the coil changes producing an induced voltage
  As the magnetic or coil rotates, it produces an alternating current (AC) {due to the changing orientation of the coil and the magnetic field}
  Types of generators:
    Turbine driven (turbo-) generators
    Magnetohydrodynamic generators (MHD)

## Slide 5: Michael Faraday (1791-1867)
A self-trained English physicist
Perhaps the greatest experimenter who ever lived
Note: since he was self taught, he did not grasp mathematics!!!
Major contributions to physics:
  Developed the concept of fields (electric and magnetic) or as he called them, “lines of force”
  invented the dynamo (a device capable of converting electricity to motion)
  discovered electromagnetic induction
  devised the laws of chemical electrodeposition of metals from solutions

## Slide 6: Transformers
Devises that utilize electromagnetic induction to increase or decrease the maximum voltage of an AC power source
Key features:
  Primary coil (input): connects to AC power source & generates the magnetic field
  Secondary coil (output): connects to the “load circuit” & reacts to the magnetic field produced by primary coil
Relationship between primary coil and secondary coil:
where:
  V is the voltage of primary or secondary coil
  N is the number of coils in primary or secondary coil

## Slide 7: Transformers (cont.)
Transformers obey conservation of energy law:
Powerprimary = Powersecondary
Power input at primary coil will always be greater or equal to the power output at the secondary coil

## Slide 8: Power Transmission
To transport electric power over large distances:
  voltages are stepped up
  Currents are stepped down
Power = Voltage x Current
  or
P = V.I
Lower currents result in less power loss (due to heat)
Transformers (at front end) are used to step up the voltage and lower current
Transformers (at back end) are used to step down the voltage and increase current for consumer usage

## Slide 9: Field Induction
Faraday’s Law in terms of fields:
  An electric field is induced in any region of space in which a magnetic field is changing with time
  E ~ B/t
  The direction of the electric field is at right angle to the changing magnetic field
Maxwell’s counterpart to Faraday’s Law:
  A magnetic field is created in any region of space in which an electric field is changing with time
  B ~ E/t
  The direction of the magnetic field is at right angle to the changing electric field