## Slide 1: Phy 202: General Physics II
Ch 15: Thermodynamics

## Slide 2: Sadi Carnot (1796-1832)
French engineer
Published only 1 work during his lifetime
  Described the details of the “Carnot” engine (an “ideal” heat engine)
Fascinated with steam engines
  Resented the advancements made in rival England
  The bulk of his work focused on understanding heat and steam engine design/efficiency
  Work based on the “caloric” theory
Contracted cholera and died the next day, at the age of 36

## Slide 3: Laws of Thermodynamics
0th Law: when 2 objects are in thermodynamic equilibrium independently with a 3rd object, they are in fact in thermodynamic equilibrium with each other or in other words,
You can use a thermometer to measure the temperature of something
1st Law: conservation of energy
U = Q - W
2nd Law: thermodynamic limit of heat engine efficiency
  Heat only flows spontaneously from high T to cold T
  A heat engine can never be more efficient that a “Carnot” engine operating between the same hot & cold temperature range
  The total entropy of the universe never decreases
3rd Law: it is not possible to lower the temperature of a system to absolute in a finite number of steps
It is impossible to reach the temperature of absolute zero

## Slide 4: Pressure-Volume Graphs
Useful visual display of a gas system
Demonstrate the work performed during a thermodynamic cycle
  Area under the PV curve is the work performed
The graphs on the right are PV curves performed at constant temperature (T)
1000 K
300 K

## Slide 5: Thermodynamic Processes (for gases)
Isothermic: constant temperature
  T = 0 means U = 0 (U is constant!)
Isochoric (or isovolumetric): constant volume
  V = 0 means W = 0 (no work performed on/by system)
Isobaric: constant pressure
  P = 0 means W = PV
Adiabatic: no gain/loss of heat energy (Q)
  Q = 0 means U = W

## Slide 6: Isothermic Processes
Process where the temperature (T) of the working substance remains constant
There are 2 possible outcomes
  As work is performed on the working substance, it releases the energy as heat (Q) {Q is released}
  All heat energy (Q) absorbed is converted to work by the working substance {Q is absorbed}
Since T = 0, then U = 0 so
U = Q – W = 0
becomes
W = Q = (nRT)ln(Vf/Vi)
{work performed by working substance}

## Slide 7: Isochoric Processes
Process where the volume (V) of the working substance remains constant
No work is performed during this process since V = 0 {area under PV curve is zero}
Two outcomes:
  Internal energy (U) increases as heat energy (Q) is absorbed by the working substance
  Internal energy (U) decreases as heat (Q) is released by the working substance
Since V = 0 then W = 0, so
U = Q

## Slide 8: Isobaric Processes
Process where the pressure (P) of the working substance remains constant
Since P = 0, then the area under the PV curve (the work performed) is equal to P.V or
W = P.V
{work performed by working substance}
The internal energy change of the system is equal to the difference between heat energy absorbed & work performed, or
U = Q – W = Q - P.V
The internal energy change (U) is also related to the change in temperature (T):
U = (3/2)nR.T {monatomic gas}
Or U = (5/2)nR.T {diatomic gas}

## Slide 9: Adiabatic Processes
Process where no heat energy (Q) is allowed to enter or leave the system, Q = 0 (U = Q – W = -W)
Two outcomes:
  Work performed on the working substance increases its internal energy by exactly the same amount
  Worked performed by the working substance decreases its internal energy by exactly the same amount
Since U = -W & U depends on T,
  For a monatomic gas:
W = - (3/2)nRT
  For a diatomic gas:
W = - (5/2)nRT

## Slide 10: P-V relation for Adiabatic Processes
When a gas undergoes an adiabatic expansion/contraction the relationship between pressure and volume is
PiVi = PfVf
where  is CP/CV (the ratio the molar heat capacities at constant P and V, respectively)
For monotomic gases,  is 5/3
For monotomic gases,  is 7/5

## Slide 11: Specific Heat Capacity & 1st Law of Thermodynamics (for diatomic gases)
The heat (Q) absorbed by a gas can be expressed as:
Q = CnT
where C is the molar heat capacity (J/mol.K)
Since gases it is necessary to distinguish between molar heat capacity at constant pressure (CP) and constant volume (CV)
Let’s begin with the 1st Law of Thermodynamics:
Q = U + W
At constant pressure: {U = (3/2)nRT & W = PV = nRT}
Q = (3/2)nRT + nRT = (5/2)nRT  CP = (5/2)R
At constant volume: {U = (3/2)nRT & W = 0}
Q = (3/2)nRT + 0 = (3/2)nRT  CV = (3/2)R
Notes: 
CpCV
“” = Cp/CV = 5/3

## Slide 12: Heat Engines
A process that utilizes heat energy input (Qin) to enable a working substance perform work output
Heat energy input equals the work performed plus the heat energy discarded:
Qin = Qout + W
Qin
W
Qout
Heat Engine

## Slide 13: Example of Heat Engine
The Carnot Cycle (Engine)
  An “ideal” reversible heat engine (no heat engine can be more efficient than a Carnot engine)
  A 4 stage engine that operates between 2 temperature reservoirs (Thot and Tcold) consisting of
    2 isothermic phases
    2 adabatic phases

## Slide 14: Efficiency of a Heat Engine
A measure of the effectiveness of a heat engine is its thermodynamic efficiency:
Efficiency =  = Wperformed/Qinput = (Qinput– Qout)/Qinput
or
% Efficiency = %  = (Wperformed/Qinput).100%
For the Carnot (“ideal”) engine:
% Efficiency = % Carnot = (Qinput– Qout)/Qinput
since Qinput/Qout = Thot/Tcold the efficiency can be written as
% Carnot = [(Thot-Tcold)/Thot ].100%

## Slide 15: Entropy
A measure of the disorder (or randomness) of a system
For a reversible the change in entropy is measured as the ratio of heat gained to temperature
S = (Q/T)R = Sfinal - Sinitial
  When heat energy is gained by a system, entropy is gained by the system (and lost by the surrounding environment)
  When heat is lost by a system, entropy is lost by the system (and gained by the surrounding environment)
The net entropy change by the universe due to a thermodynamic process:
Suniverse = Sgained - Slost = Qcold/Tcold - Qhot/Thot
The total entropy of the universe (Suniverse) will never decrease, it will either
  Remain unchanged (for a reversible process)
  Increase (for an irreversible process)
Change in entropy is related to the amount of energy that is lost irretrievably by a thermodynamic process:
Wunavailable = TcoldSuniverse
Notes: Entropy is a state function (like energy)
Changes in entropy occur independent of path taken by the system