## Slide 1: Phy 213: General Physics III
Chapter 26: Electric Current
Lecture Notes

## Slide 2: Electric Current
An electric potential causes electric charges to move
The flow of electric charge is called electric current
  Positive charge accelerates toward lower electric potential
  Negative charge accelerates toward higher electric potential
The rate of flow of electric charge (i) through a conducting material is
The SI units are coulombs per second (C/s), called amperes (A): 1 C/s = 1 A
The quantity of charge movement (q) is related to the electric current (i):
Note: By convention, electric current is defined as the flow of positive charge carriers flowing from high potential (+) to low potential (-)
Notes: Direct current (DC): I = dq/dt = constant
Alternating current (AC): I = varying value

## Slide 3: Conduction Model of Electric Current (through a constant area pathway)
Conduction depends on potential difference between 2 regions & how far apart those regions are separated
Increasing the cross-sectional area increases amount of charge that can flow through in a given time, for constant J
Of course, the relative ability to conduct charge is an intrinsic property of different materials !!
VB
L
VA
i
L
VA
A
i
VB
Notes: Consider conduction through 2 layers of different materials

## Slide 4: Conduction of Electric Current (cont.)
The rate of charge flow (current) w/in a conductor depends on
  The potential difference between 2 regions along the conducting pathway material (V)
  The cross sectional area of the conducting pathway (A)
  The ability of the conductor to conduct charge () {the conductivity}
  The length of conducting pathway (L)
For a uniform cylindrical conductor, combining these elements leads to the conduction equation:
The quantity, , is called the conductivity (g):
Conductivity is more commonly expressed as the “resistance” (R) of the conducting pathway:
where r is the “resistivity “ (in units of or )

## Slide 5: Current Density & Drift Velocity
The current density of charge flow through a cylindrical region (area, A and length L) is related to the number of charge carriers (n) & their average drift velocity (vdrift):
For a 0.1A current flowing through a copper wire (n = 8.49x1028m-3 & A = 1x10-6 m2):
For a steady state uniformly distributed electric current, the current can be expressed in terms of its associated current density vector (J).
where is the area vector, perpendicular to the cross sectional area through which the current flows
L
A
Notes: n = (#conducting electrons/atom)x(density)x(avogadro’s number)/(molar mass)

## Slide 6: Ohm’s Law
The electric current can be re-expressed as:
where V = V = the potential difference across the conductive pathway
Thus, the current through any conducting pathway can be described by dividing the potential across the pathway by the effective resistance of the pathway…
Or
The resistance of a conducting pathway is defined as the potential difference divided by the current flow:
When the ratio, V/i, is a constant value for all values of V the conductor is said to be an “Ohmic” material:
V/i = R = constant {Ohm’s Law}
When R is not constant, the conductor is non-Ohmic
Ohm’s Law is more commonly expressed as: V = iR

## Slide 7: Resistance
The resistance (R) of a substance depends on:
  length (L)
  Cross-sectional area (A)
  Resistivity ()  units are .m
Units of resistance are V/A, called ohms ()
1 V/A = 1 
The intrinsic physical property, resistivity () depends on temperature. Over a limited temperature range the temperature dependence is given by:
  For conductors: resistivity increases with T ( > 0)
  For semi-conductors: resistivity decreases with T ( < 0)
Notes: For resistivity: T can be expressed in either oC or K
 is + (for conductors) & - (for insulators)

## Slide 8: Table of Selected Resistivities (@ 20oC)
Material |  ( m) | oC) | Material |  ( m) | oC)
Silver | 1.59x10-8 | .0061 | Carbon* (graphite) | 3-60x10-5 | -.0005
Copper | 1.68x10-8 | .0068 | Germanium* | 10-3-10-1 | -.05
Aluminum | 2.65x10-8 | .00429 | Silicon* | 0.1-60 | -.07
Tungsten | 5.6x10-8 | .0045 | Glass | 109-1013 | ...
Iron | 9.71x10-8 | .00651 | Quartz (fused) | 7.5x1017 | ...
Platinum | 10.6x10-8 | .003927 | Hard rubber | 1013-1015 | ...
Manganin | 48.2x10-8 | .000002 |  |  | 
Lead | 22x10-8 | 0.0039 |  |  | 
Mercury | 98x10-8 | .0009 |  |  | 
Table reproduced from: http://hyperphysics.phy-astr.gsu.edu

## Slide 9: Relation between Current Density & Resistance
The resistivity of a conducting material, reflects the ability of the material to resist current flow and thus limit current density, for a given potential difference:
where  = V/L (the potential difference per unit length)
Semi-Obvious Consequence:
For steady state current flow, as the current density increases and surface area decreases:
=constant→V/L must increase→ V will increase
→R must increase

## Slide 10: Power
It requires energy to “push” charge through an electrical device. This should be obvious given that the charge flows from high potential (Uhigh) to lower potential (Ulow).
The energy must go somewhere if the charge flows at constant drift velocity (K=0). It is radiated out as heat energy.
The energy transfer associated with moving a charge dq across a potential difference, V is:
The rate of energy transfer, in Watts, is given by:
Applying Ohm’s Law, the power can be alternatively expressed to describe “resistive” dissipation of energy: