## Slide 1: Phy 213: General Physics III
Chapter 27: Electric Circuits
Lecture Notes

## Slide 2: Electromotive Force & Internal Resistance
The intrinsic potential difference associated with a power source is referred to as the “electromotive force” or emf
  In an ideal power source, the voltage across its terminals is its emf
  For a real power source, such as a battery, the emf is determined by the net electrochemical potential due to its internal redox reaction BUT the actual voltage across its terminals is slightly lower due to its internal resistance (Rint).
Real power sources are limited in their ability to deliver power output, due to factors such as the maximal rate of the internal chemical reaction, the input power (in an AC plug-in DC power source), etc…
  For a battery, the rate of reaction is dependent on the conditioning and corrosion of electrodes and depletion of internal reactants. This results establishes an effective internal resistance, within the voltage source.
As an electrochemical power source is utilized and is run down, the decline in performance output is reflected in the increased in internal resistance
  The output voltage will wane as more of the potential drops across Rint even though the emf remains constant
Rint
+
-
+
-
emf
V

## Slide 3: Kirchoff’s Voltage & Current Laws
Example: A single loop circuit where R1=R2=R3=10
Kirchoff’s Current Law (aka the Node Law):
The total current through any node is equal to zero:
Kirchoff’s Voltage Law (aka the Loop Law):
For any closed loop in a circuit, the total voltage around the loop is equal to zero:
+
-
10V
R1
R3
R2
i1
i3
i2

## Slide 4: Series Circuits
In series wiring, circuit elements (loads) are connected end to end
The combined load or resistance (Req) in the series is
Across each resistance, the potential difference (V) drops
The current i that flows through R1 also flows through R2
V = V1 + V2 = iR1 + iR2
or
V = i(R1 + R2)= iReq
V

## Slide 5: Parallel Circuits
Circuit elements (loads) are connected with ends attached
The combined load or resistance (Rp) in the parallel is
Across each resistance, the potential difference (V) is the same
The total current drawn through the circuit is: i = i1 + i2
or

## Slide 6: Analyzing Circuits 1 (using Kirchoff’s Laws)
Consider the following 2 loop circuit, with 6 equal value resistors (R=R1=R2=R3=R4=R5=R6=10:
What is the current & voltage for each R?
  a. Kirchoff’s Laws:
  Loop 1:
  Loop 2:
  Node:
solving for i’s:
R6
R3
+
-
10V
R1
R2
R4
R5
1
2
i1
i3
i2
i1

## Slide 7: Analyzing Circuits 2 (using equivalent resistances)
Consider the same circuit:
What is the current & voltage for each R?
  a. Solve for Req1:
  b. Solve for Req2:
  c. Solve for Req:
  Use Req to get i1 & Req2 to get VR1& VR3
  Solve for the rest:
R3
+
-
10V
R1
R2
Req1
R3
+
-
R1
Req2
+
-
Req

## Slide 8: RC Circuits
A circuit containing a capacitor and resistor(s) is called an RC circuit
A resistor in series with a capacitor will limit the rate (not quantity) at which charge accumulates in the capacitor
When V is constant across a capacitor ( = 0) no current will flow through this branch of the circuit since:
C
R
When a fully charged capacitor is discharged, the rate of charge loss is limited by the voltage across it and is limited by on the resistance:

## Slide 9: Charging a Capacitor
The voltage equation around a loop with resistor and capacitor in series with a constant voltage source is given by:
Re-arranging the equation leads to a 1st order linear non-homogeneous differential equation. This can be solved by applying the separation of variables technique:
C
V
R

## Slide 10: Capacitive Charging & Discharging (C=0.1F, Vmax=10V & R=10)

## Slide 11: Capacitive Charging in RC circuit (Effects of increasing R on Vcap)
Charging
Discharging

## Slide 12: Capacitive Charging (i vs t)
Charging
Discharging
What should these graphs should look like?